## Slide 1
LITERATURE READING SECTION
AMZ Driverless:
The Full Autonomous Racing System
A review of the perception, estimation, planning, and control system behind
ETH Zürich's Formula Student Driverless racecar — Kabzan et al., 2019
Yassin • ARL Formula 2027 Mission — Literature Reading

## Slide 2
CONTEXT
Racing a Track the Car Has Never Seen
Formula Student Driverless: student-built racecars compete fully autonomously, with no driver and no prior map of the track.
The car must perceive cones marking the track edges, estimate its own motion, build a map, and control itself — all in real time.
AMZ Driverless (ETH Zürich) finished 1st overall at every competition entered: FS Germany 2017, FS Italy 2018, FS Germany 2018.
Two Operating Modes
SLAM MODE
Perceive cones, build the map,
and localize simultaneously
LOCALIZATION MODE
Map is frozen after lap 1 —
race as fast as possible
Triggered by lap closure detection
Modules: Perception → Motion Estimation & Mapping → Control
02

## Slide 3
SYSTEM OVERVIEW
Sensors to Actuators, End to End
SENSORS
LiDAR · Stereo & Mono Camera · IMU · GNSS · Wheel Speed Sensors
PERCEPTION
LiDAR cone pipeline + Camera cone pipeline (independent & redundant)
MOTION ESTIMATION & MAPPING
Velocity EKF → FastSLAM 2.0 → Boundary Estimation
CONTROL
Nonlinear MPC → Low-level torque distribution → Steering / Throttle / Brake
03

## Slide 4
PERCEPTION — LIDAR
From Raw Point Cloud to Colored Cones
PRE-PROCESSING
Ground removal +
motion-distortion correction
CONE DETECTION
Euclidean clustering +
cluster reconstruction
COLOR ESTIMATION
CNN on intensity
pattern per cone
Why motion distortion matters (critical)
A LiDAR scan isn't captured in a single instant — points are collected as the sensor sweeps, while the car keeps moving. If that motion isn't accounted for, the resulting point cloud is warped, distorting cone shapes or even creating “ghost cones.” The car's own velocity estimate is used to undistort each scan before detection runs.
Ground removal strips away most of the ground plane — but also strips many real cone points, since cones are small and sparse in the point cloud.
Cluster reconstruction recovers this: a cylindrical region is rebuilt around each detected cluster center using the pre-ground-removal points, restoring enough points for reliable detection and color estimation.
04

## Slide 5
PERCEPTION — LIDAR
Estimating Cone Color from Light Intensity
Cones have a real physical pattern: yellow cones are yellow-black-yellow, blue cones are blue-white-blue.
As the LiDAR beam scans vertically up a cone, these color bands reflect light differently — producing a distinct high-low-high or low-high-low intensity gradient.
That intensity pattern (not visible color, since LiDAR has none) is mapped into a small 32×32 grayscale image and fed to a CNN.
The CNN outputs a probability the cone is blue, yellow, or unknown — trained with a loss that punishes blue↔yellow mix-ups far more than an “unknown” call.
Why this matters
Color tells the car which side of the track a cone marks (blue = left, yellow = right), which the boundary and planning modules depend on directly.
Result
96% accuracy on familiar cones, and — unlike a simple rule-based gradient check — the CNN stays reliable even on cones it wasn't trained on (e.g. cones with stickers altering their intensity pattern).
05

## Slide 6
PERCEPTION — CAMERA
Monocular vs. Stereo: Two Ways to Find 3D Cones
Shared first step — YOLOv2 detects & classifies cones (blue / yellow / orange) as 2D bounding boxes
MONOCULAR PIPELINE
CNN regresses 7 known “keypoints” on the cone (corner-like features) from a single image.
Since one image alone can't resolve depth, the cone's known real-world size/shape is used as a geometric prior.
PnP (Perspective-n-Point) matches the 2D keypoints to their 3D prior to estimate the cone's full 3D pose.
STEREO PIPELINE
Detection runs only on the left frame; the bounding box is propagated to the right frame using stereo geometry.
SIFT features are matched between the left/right boxes — chosen over BRISK for fewer mismatches.
Matched points are triangulated directly for 3D position — no size/shape prior needed, and generally lower variance than PnP.
06

## Slide 7
PERCEPTION — AS A WHOLE
Why Two Independent Pipelines
Sensor Redundancy
LiDAR and camera pipelines run fully independently, at both hardware and software level.
Each sensor has different failure modes — a camera can be blinded by glare, LiDAR struggles with tiny/distant cones — so redundancy means one failing doesn't blind the car.
Both pipelines feed the same SLAM map, so the system tolerates a single-sensor failure without stopping.
Validated Results
LiDAR color estimation: 96% accuracy on familiar cones; robust even on unfamiliar (sticker-modified) cones.
Camera-vs-LiDAR position error stays under 1.0 m even at 15 m range.
Stereo position estimates have lower variance than monocular (PnP) estimates.
Vision-only SLAM map RMSE of just 0.25 m against ground-truth survey positions.
07

## Slide 8
MOTION ESTIMATION
Why the Car Must Know Its Own Motion
Velocity feeds three different downstream systems: undistorting LiDAR scans, propagating the SLAM motion model, and the control loop itself.
No single sensor measurement can be fully trusted alone — every sensor has its own bias, noise, and failure characteristics.
A 9-state Extended Kalman Filter (EKF) fuses six different sensors together, using a vehicle/tire-slip model to predict, then correcting with real measurements.
Fused into the EKF
Motor torque + steering angle — process model inputs
Tire-slip model — model-based acceleration estimate
IMU — acceleration, yaw rate
GNSS — global position/velocity
GSS — ground speed sensor
WSS — wheel speed sensors (all 4 wheels)
State observability is analyzed explicitly: the system stays observable even if GSS or GNSS alone fails — a deliberate robustness design choice.
08

## Slide 9
MOTION ESTIMATION
Two Failure Types Need Two Detectors
OUTLIERS
Sudden spikes in a single measurement — one bad reading, then back to normal.
Detected with a Chi-square test — works well, catching bad readings immediately as they happen.
DRIFT
A slow, gradual departure from the truth — each single reading looks almost fine.
The Chi-square test alone catches this too late — only once the error has already grown large. A variance-based check across redundant sensors is used instead, progressively rejecting whichever sensor contributes most to rising disagreement.
Both detectors run alongside each other — neither alone is sufficient.
09

## Slide 10
SLAM & MAPPING
Why the Car Needs SLAM at All
The track is unknown at the start — there is no pre-existing map to localize against.
But the car needs to “see” roughly 2 seconds ahead (~40 m at race speed) — well beyond what its raw sensor field of view provides in a single instant.
SLAM solves this: build the map of cones and localize the car within that same growing map, simultaneously.
The Data Association Problem
Cones aren't individually distinguishable — they only carry a position and a color, and many cones share that same color. So every time a cone is (re)observed, the system must decide which existing map landmark it corresponds to — or whether it's new — under real ambiguity. This uncertain matching is the core challenge SLAM has to handle here.
10

## Slide 11
SLAM & MAPPING
FastSLAM 2.0 and Lap Closure
FastSLAM 2.0
A particle-filter based SLAM algorithm — each particle carries its own full hypothesis of the car's pose and the map.
This naturally handles multiple competing data-association guesses at once, instead of committing to one.
Scales linearly with the number of landmarks, versus the quadratic cost of EKF-SLAM — a major performance advantage for a track full of cones.
Lap Closure
Detected once three conditions hold: particle spread is low, current heading matches the start, and particles cluster near the starting point.
Once detected, the system switches from SLAM mode to Localization mode — the map is frozen (taken from the highest-weight particle) and stops updating.
From then on, Monte Carlo Localization is used to localize within that fixed map for the remaining, fast laps.
11

## Slide 12
PLANNING
Turning Cones into Candidate Paths
1. TRIANGULATE
Delaunay triangulation over
observed cone positions
2. GROW PATH TREE
Connect midpoints of triangle
edges, breadth-first
3. SCORE & SELECT
Rank by cost function,
pick lowest-cost path
There's no single fixed goal position — instead, the space between left and right cones defines a whole set of possible center-line paths.
The car doesn't need a full map upfront: this runs in a receding-horizon fashion, re-estimating a new candidate center line roughly every 50 ms as new cones come into view.
The worst candidate paths are pruned along the way (beam search) to keep the search computationally tractable in real time.
12

## Slide 13
PLANNING
Scoring Candidate Paths
Max angle change
Sharp direction changes are unlikely — even hard corners are built from multiple cones.
Track width consistency
Track width is rule-regulated, so it shouldn't vary much along a valid path.
Left/right cone spacing
Cones marking the track are roughly evenly spaced — helps discard outlier detections.
Wrong-color probability
Left cones should be blue, right should be yellow — penalizes paths that break this.
Path length vs. sensor range
Penalizes paths that are implausibly shorter or longer than the sensor's range.
All five costs are normalized, squared, weighted, and summed — the lowest-cost path is chosen as the estimated center line and track boundary.
13

## Slide 14
CONTROL
Racing Isn't Just Following the Center Line
The goal in Control mode isn't to stay safely centered — it's to minimize lap time, which is a fundamentally different objective.
The fastest racing line often cuts closer to one edge through corners, trading extra path length for a higher sustainable speed — something a pure center-line follower would never do.
The system uses a nonlinear Model Predictive Control (MPC) framework that directly maximizes progress along the track, while respecting the vehicle's real handling limits and the track boundaries — with no separate, pre-computed “racing line” logic needed.
Why MPC specifically
MPC looks ahead over a prediction horizon and directly accounts for the vehicle's traction limits and track constraints while computing each command — rather than reacting only to the current instant, or relying on hand-tuned racing-line heuristics.
14

## Slide 15
CONTROL
The Bicycle Model Feeding the MPC
Bicycle Model
A simplified vehicle model (two wheels instead of four) that captures mass, inertia, and nonlinear tire forces — accurate enough for racing, simple enough to solve in real time.
Blends a dynamic model (accurate at speed) with a kinematic model (stable at low speed, e.g. race starts and sharp corners) — using whichever suits the current speed.
Includes a tire “friction ellipse” constraint, so the car can't be commanded to exceed real available grip.
MPC Loop
Follows the planned center line via a “contouring” cost: minimizes how far off the path the car is, while maximizing progress along it.
Track boundaries are enforced as circular constraints along the path, keeping the car provably inside the track.
Solved in real time — 90% of solves finish under the 0.05s control period, with a worst case of 0.065s.
15

## Slide 16
TESTING & SIMULATION
Catching Failures Before the Track
Why Simulate First
Real-world testing costs real time and manpower, and heavily limits how many tests can actually be run.
Simulation (FSSIM, built on Gazebo with a custom first-principles vehicle model) runs automatically on every code change and every night.
Direct cone observations with realistic noise are simulated — sensor-level simulation is skipped to keep it fast and lightweight.
Automated Testing System (ATS)
Every test/simulation run produces large volumes of logged data (rosbags) — far too much to review manually.
A bookkeeping service queues and distributes simulation and visualization tasks to worker nodes automatically.
Results are indexed and visualized through a web interface, and failures trigger automatic notifications — shortening the iteration loop and catching regressions early.
16

## Slide 17
TAKEAWAY
One Integrated System, Proven on Track
Redundant perception (LiDAR + camera), a fault-tolerant 9-state EKF for motion, particle-filter SLAM, and nonlinear MPC control are combined into one real-time racing stack.
The result: 1st place overall at every Formula Student Driverless competition entered — proof the system reliably races and finishes on previously unknown tracks.
The consistent design theme across every module: assume any single sensor or estimate can fail, and build in redundancy and failure detection accordingly.
17

## Slide 18
DISCLOSURE
How AI Was Used
Claude was used to help structure this presentation: organizing the paper's content, and designing the visual template.
I am prepared to discuss every point in this deck directly in the interview.
18